## Slide 1
www.bennettcustomaudio.ca
bennettcustomaudio@gmail.com
“Chinook”
Custom Dual Overdrive
Introduction:
This custom-designed pedal features two independent overdrive circuits with order switching. The overdrives are modified versions of the Boss BD2 (“BD2”), and the Zendrive by Hermida Audio (“Zendrive”). The Chinook must be powered by a 9-18VDC, centre-negative power supply, capable of delivering 100mA of current – It does not have room for a battery inside. Like all our pedals, The Chinook was designed and assembled by hand in St. John’s, NL.
Controls:
BD2 VOL: Controls the output level of the BD2. Turn it up for a louder signal.
BD2 GAIN: Determines the amount of distortion in the BD2. Turn it up for a more distorted, sustaining tone with more harmonics. Turn it down for a cleaner sound.
BD2 BASS: Controls the amount of bass in the BD2. It has a centre-notch for a flat response, and may be boost or cut from there by turning it up or down.
BD2 MIDS: A 3-position switch that sets the mid-range response of the pedal. The CENTRE position gives a flat response. DOWN gives a scooped mid, and UP gives a pushed mids response.
BD2 TREBLE: Controls the amount of treble in the BD2. It has a centre-notch for a flat response, and may be boost or cut from there by turning it up or down.
ZEN VOL: Controls the output level of the Zendrive. Turn it up for a louder signal.
ZEN GAIN: Determines the amount of distortion in the Zendrive. Turn it up for a more distorted, sustaining tone with more harmonics. Turn it down for a cleaner sound.
ZEN TONE: Controls how warm or bright the tone will be. Turn it up for a bright sound.
ZEN VERSION SWITCH: Sets the “version” of the Zendrive. Version I is brighter, with asymmetric clipping, less bass, and less overall gain. Version II has more gain, bass, and symmetric clipping for a warmer, fuzzier tone.
ZEN VOICE: Sets the pre-gain bass of the Zendrive. Turning it down gives a warmer, less distorted sound. Turning it up gives a brighter sound with more overall gain.
BD2 Footswitch: Toggles the BD2 on or off with true bypass. IF the LED next to it is illuminated, your signal is passing into the effect.
Order Switch: Sets the order of the two overdrive circuits. UP puts the Zendrive before the BD2 in your signal chain, DOWN puts the BD2 before the Zendrive.
ZEN Footswitch: Toggles the Zendrive on or off with true bypass. IF the LED next to it is illuminated, your signal is passing into the effect.
V1.0.0